# Installing AREDN® Firmware
There are two cases for installing AREDN® firmware:
1. If you already have an existing version of AREDN® running on your device, then you can use your computer’s web browser and navigate to Setup > Administration > Firmware Update to install your new firmware. This process will be explained in more detail in the Configuration Deep Dive section of this guide. Also, see Firmware Upgrade Tips in the How-to Guides section for additional information.
2. If you are installing AREDN® firmware on a device for the first time, each hardware platform may require a unique procedure.

## Firmware First Install Checklists
It may be helpful to have a brief checklist of steps to follow when doing the initial firmware installation on node hardware. The checklists below are provided to assist with this process, based on the manufacturer of your device. Complete step-by-step instructions are detailed in the sections that follow.
GL.iNet First Install Checklist (PDF)
## GL-iNet First Install Process
GL-iNet devices allow you to use the manufacturer’s pre-installed OpenWRT web interface to upload and apply new firmware images. Check the GL-iNet documentation for your device if you have questions about initial configuration. Both GL-iNet and AREDN® devices provide DHCP services, so you should be able to connect your computer and automatically receive an IP address on the correct subnet. GL-iNet devices usually have a default IP address of 192.168.8.1, so if for some reason you need to give your computer a static IP address you can use that subnet.
After the GL-iNet device is first booted and configured, navigate to the Upgrade section and click Local Upgrade to select the AREDN® sysupgrade.bin file you downloaded for your device.
Attention
Be sure to uncheck the Keep Settings checkbox, since GL.iNet settings are incompatible with AREDN® firmware.
The node will automatically reboot with the new AREDN® firmware image. If for some reason your GL-iNet device gets into an unusable state, you should be able to recover using the process documented here: GL-iNet debrick procedure
## After the Firmware Install
After the node reboots, it should have a default IP address of 192.168.1.1. You should be able to ping the node at 192.168.1.1. Don’t proceed until you can ping the node. You may need to disconnect and reconnect your computer’s network cable to ensure that it has a connection.
Open Windows PowerShell from Windows menu. Type at the prompt [PS C: ...>] “ping 192.168.1.1”
Display should read:
Pinging 192.168.1.1 with 32 bytes of data:
Reply from 192.168.1.1 bytes=32 tine<1ms TTL=64
Once your device is running AREDN® firmware, you can display its web interface by navigating to either http://192.168.1.1 or http://localnode.local.mesh . Some computers may have DNS search paths configured that require you to use the fully qualified domain name (FQDN) to resolve localnode to the mesh node’s IP address. You may need to clear your web browser’s cache in order to remove any cached pages.
You can use your web browser to configure the new node with your callsign, admin password, and other settings as described in the Basic Radio Setup section of the documentation.
Link: AREDN Webpage