Charts recorded as CHART(X). JPG

Figure 1: Chart 0
Figure 2: Chart1

Figure 3: Chart 2

Figure 4: Chart 3

Figure 5: Chart 4
Figure 6: Chart 5 ..Same beginning as Chart 4
Sequence

1. Same amp antenna on both GL150 nodes with 18dBm. Separation 30 ft 7 in
Noticed that a 1 ft offset from centerline between the narrow width of the antenna increases the SNR by about 6 dB
2. Add Amp to K1YBE, (Error made with chart average)
3. Add Amp to KB1ZZU
4. Remove Both Amps
5. Add 5 element Yagis to both nodes.
Noticed:
Height above table improved SNR
Large drop for cross polarization (last dip in chart 5)
Same SNR for Horiz or Vertical polariztaion

Note that changing one amp at a time, allows for separating the RX preamp affect using change in level at the remote end

Table to predict the SNR from .25 mi to 56 mi using the 30’7” Reference

				20 log10(f)	20 log10(4π/c)		Predicted
d(miles)	d(yds)	d(m)	20log10(d)	2.40E+09	-147.56	FSPL	SNR @ d(r)
Reference	10.19440	9.32	19.39	187.60	40.05	59.44	60.0
0.25	273	249.17	47.93	187.60	40.05	87.98	31.5
0.50	545	498.35	53.95	187.60	40.05	94.00	25.4
0.75	818	747.52	57.47	187.60	40.05	97.52	21.9
1.00	1,090	996.70	59.97	187.60	40.05	100.02	19.4
1.25	1,363	1,245.87	61.91	187.60	40.05	101.96	17.5
1.50	1,635	1,495.04	63.49	187.60	40.05	103.54	15.9
1.75	1,908	1,744.22	64.83	187.60	40.05	104.88	14.6
2.00	2,180	1,993.39	65.99	187.60	40.05	106.04	13.4
2.25	2,453	2,242.57	67.01	187.60	40.05	107.06	12.4
2.50	2,725	2,491.74	67.93	187.60	40.05	107.98	11.5
2.75	2,998	2,740.91	68.76	187.60	40.05	108.80	10.6
3.00	3,270	2,990.09	69.51	187.60	40.05	109.56	9.9
3.25	3,543	3,239.26	70.21	187.60	40.05	110.25	9.2
3.50	3,815	3,488.44	70.85	187.60	40.05	110.90	8.5
3.75	4,088	3,737.61	71.45	187.60	40.05	111.50	7.9
4.00	4,360	3,986.78	72.01	187.60	40.05	112.06	7.4
4.25	4,633	4,235.96	72.54	187.60	40.05	112.59	6.9
4.50	4,905	4,485.13	73.04	187.60	40.05	113.08	6.4
4.75	5,178	4,734.31	73.51	187.60	40.05	113.55	5.9
5.00	5,450	4,983.48	73.95	187.60	40.05	114.00	5.4
5.25	5,723	5,232.65	74.37	187.60	40.05	114.42	5.0
5.50	5,995	5,481.83	74.78	187.60	40.05	114.82	4.6
5.75	6,268	5,731.00	75.16	187.60	40.05	115.21	4.2
6.00	6,540	5,980.18	75.53	187.60	40.05	115.58	3.9